## Slide 1: ENVE 201 Environmental Engineering Chemistry 1
Alkalinity
Dr. Aslıhan Kerç

## Slide 2: ALKALINITY
Alkalinity : Capacity of a water to neutralize acids.(Acid neutralization capacity)
Alkalinity in natural waters
Due to salts of weak acids
Weak or strong bases

## Slide 3
Major form of alkalinity bicarbonates
CO2 + CaCO3 + H2O  Ca2+ + 2HCO-
Formed with the rxn of CO2 and basic materials in soil.
Organic acid salts
Salts of weak acid (in anaerobic waters acetic , propionic)
Ammonia

## Slide 4
Natural waters may contain carbonate and hydroxide alkalinity.
Algae remove CO2  pH 9-10
Boiler waters contain CO3= and OH- alkalinity
Types of alkalinity in natural waters :
Hydroxide
Carbonate
Bicarbonate

## Slide 5
Alkalinity acts as buffer to resist to pH drops
No public health significance of alkalinity
Taste of highly alkaline waters are not good

## Slide 6
Methods of Determining Alkalinity
Titration with N/50 H2SO4 reported in terms of equivalent CaCO3.
If pH > 8.3 Titration in two point
First step  till pH 8.3 phenolphthalein turning point ( pink to colorless)

## Slide 7
Second step  pH 4.5 Bromcresol green end point or M.O.
@ pH 8.3 CO2-3 + H+ HCO-3
@ pH 4.5 HCO-3 + H+ H2CO3
Alkalinity is the sum of all the titratable bases
0.01 M [HCO-3 ]  500 mg/L as CaCO3
10 meq/L * 50 mg/meq = 500 mg/L

## Slide 8
Titration curve for a hydroxide-carbonate mixture.
Figure 18.1

## Slide 9: Phenolphthalein and Total Alkalinity
Strong base titration curve
@ pH 10 all the hydroxide ions are neutralized
@ pH 8.3 carbonate converted to bicarbonate
Titration till phenolphthalein end point Phenolphthalein alkalinity

## Slide 10
Total alkalinity  titration till pH 4.5
Conversion till carbonic acid H2CO3
Phenolphthalein Alkalinity =
mL N/50 H2SO4 * 1000/mL sample
Till pH 8.3
Total Alkalinity =
mL N/50 H2SO4 * 1000/mL sample
Till pH 4.5

## Slide 11
Calculate
Hydroxide, Carbonate, Bicarbonate alkalinity
  1. Calculation from alkalinity measurements
2. Calculation from alkalinity and pH measurement
3. Calculation from equilibrium equations (carbonic acid)

## Slide 12: Calculation from Alkalinity Measurements
Determine pp and total alkalinities.
OH- , CO=3 , HCO-3 calculated not exactly
Assumption OH- and HCO-3 cannot exist together

## Slide 13
Graphical representation of titration of samples containing various forms of alkalinity.
Figure 18.2

## Slide 14
Five possible situations :
Hydroxide only
Carbonate only
Hydroxide and Carbonate
CO=3 and HCO-3
HCO-3
@pH 8.3 neutralization of hydroxides are completed.

## Slide 15
Carbonate CO=3 is one half neutralized
2nd phase of titration :
For hydroxide negligible amount of additional acid is required.
For CO=3 , exactly equal amount of acid is required to reach pH 8.3

## Slide 16
OH- only : pH > 10
OH alkalinity = Phenolphthalein alkalinity
CO=3 only : pH > 8.5 , Vt=2Vpp
OH- and CO=3 pH > 10
CO=3 = 2(titration form 8.3 – 4.5)*1000
mL sample
Hydroxide alk. = Total- Carbonate alk.

## Slide 17
CO=3 and HCO-3 8.3 < pH < 11
Carbonate alk. = 2 * (Vpp) * 1000
mL sample
HCO-3 = Total- Carbonate alk.
HCO-3 only pH < 8.3
Bicarbonate = Total Alk.

## Slide 18: Calculation from Alkalinity + pH Measurements
Measure :
pH
Phenolphthalein alkalinity
Total alkalinity
Calculate OH- , CO=3 and HCO-3

## Slide 19
Hydroxide alkalinity  calculated from pH measurement.
[OH- ] = Kw / [H-]
1 mol/L = 50000mg/L as CaCO3
Hydroxide alkalinity = 50000 x 10(pH-pKw)
pKw = 14.00 @ 24 °C

## Slide 20
Phenolpht. alk. = Hydroxide + ½ Carbonate
Carbonate alk. = 2 ( pp alk. – hyd. Alk. )
Bicarbonate alk. = Total alk. – (carbonate alk. + hydroxide alk. )
(Titration from pH 8.3 to 4.5)
Remaining ½ carbonate alk.
Bicarbonate alk.

## Slide 21: Carbonate Chemistry
H2CO3 , HCO-3 , CO=3 , CO2 (aq)
( dissolved in water CO2 )
X CO2 = P CO2 / k CO2 (Henry’s Law)
Constituents of alkalinity in natural waters.
HSiO-3 , H2BO-3 , HPO=4 , H2PO-4

## Slide 22
HS- , NH3 , conjugate bases of organic acids
OH- , CO=3 , HCO-3
H+ + HS-  H2 S
H+ + OH-  H2 O
H+ + CO=3  HCO-3
HCO-3 + H+  H2CO3
(2 H+ + CO=3  H2CO3 )

## Slide 23
Alkalinity and acidity are based on the “carbonate system “ .
[Alk.]=[HCO-3 ] + 2[CO=3 ] + [OH-] – [H+ ]
( mol/L of H+ that can be neutralized)
(Alk.)=(HCO-3 )+ (CO=3 ) + (OH-) – (H+)
( eq/L of H+ that can be neutralized)
Alk. In mg/L as CaCO3 = ( Alk.) x EW CaCO3

## Slide 24
Example :
CO=3 = 20 g/m3 HCO-3 = 488 g/m3
OH- = 0.17 g/m3 Alk. = ?
Ion | MW ( g/mole) | EW (g/eq) | (eq/m3 )
CO=3 | 60 | 30 | 20/30=0.67
HCO-3 | 61 | 61 | 488/61=8
OH- | 17 | 17 | 0.17/17=0.01

## Slide 25
[H+ ] [ OH- ] = Kw
(OH-) (H+) =Kw
[H+ ] = 10-14 / (0,01x 1/1000 x 1 mol/eq)
= 10-9 mol/L =10-9 eq/L = 10-6 eq/m3
[Alk.]=[HCO-3 ] + 2[CO=3 ] + [OH-] – [H+ ]
(Alk.)= 8,00 + 0,67 + 0,01 - 10-6
=8,68 eq/m3
(8,68 x 10-3 eq/L) x (50000 mg/eq)=434 mg/L as
CaCO3

## Slide 26: Expressing in terms of CaCO3
Species A
mg/L as CaCO3 = ( mg/L A)(EW CaCO3 / EWA)
Example : 10 mg/L Mg2+
Mg+2 = 24,3 mg/L EW Mg+2 = 24,3/2=12,15
Conc of Mg+2 as CaCO3
(10 mg/L)x((5000 mg/eq)/(12150 mg/eq Mg+2))
= 41,15 mg/L as CaCO3

## Slide 27: Calculation from Equilibrium Equations
Equilibrium eqns
(Acidity and alkalinity are based on carbonate system)
Electroneutrality (charged balance) in sol’n
Equivalent conc. of anions = cations
Total alk. = Alkalinity producing anions – hydrogen ions

## Slide 28
[Alk.]=[HCO-3 ] + 2[CO=3 ] + [OH-] – [H+ ]
( mol/L of H+ that can be neutralized)
(Alk.)=(HCO-3 )+ (CO=3 ) + (OH-) – (H+)
( eq/L of H+ that can be neutralized)
Alk. In mg/L as CaCO3 = ( Alk.) x EW CaCO3

## Slide 29
Equilibrium equations :
Dissociation of water [OH-] = Kw/ [H+ ]
Second ionization for carbonic acid
KA2 = [H+ ] [CO=3 ] / [HCO-3 ]
[H+ ] + alkalinity = [HCO-3 ] +2 [CO=3 ] + [OH-]
50000

## Slide 30
Carbonate alk. = 50000[(alk./50000)+ [H+ ] –(Kw/ [H+ ] )]
(mg/L as CaCO3 ) 1+([H+ ] /2 KA2 )
Bicarbonate alk. =50000[(alk./50000)+ [H+ ] –(Kw/ [H+ ] )] (mg/L as CaCO3 ) 1+(2 KA2 / [H+ ] )
KA2 and Kw change with temperature and ionic conc.

## Slide 31: CO2 , Alkalinity and pH relationship
Equilibrium rxns :
CO2 + H2 O  H2CO3 [H+ ] + [HCO-3]
M(HCO-3 )2  M+ + 2 HCO-3
HCO-3  H+ + CO=3
CO=3 + H2O  HCO-3 + OH-
HCO-3 is involved in all equations.
Change in conc. or pH shift the equilibrium.

## Slide 32: pH Changes during Aeration
Aeration removes CO2
CO2 acidic gas removal increase pH
Air content 0,03 % by volume CO2
Henry ‘s constant : 1500 mg/L.atm
Equilibrium conc.for CO2 = 0,0003 x 1500
=0,45 mg/L

## Slide 33
KA1 = [H+ ] [HCO-3 ] / [H2CO3 ]
If alkalinity = 100 mg/L
Aerated until equilibrium of CO2 in air
pH=8,6

## Slide 34: pH Changes in Algal Blooms
During algal blooms pH 10
Algae use CO2 in photosynthesis.
Algae can reduce CO2 conc. below its equilibrium concentrations.
As pH increase alkalinity forms change

## Slide 35
2HCO-3  CO=3 + H2O + CO2
CO=3 + H2O  2OH- + CO2
Total alkalinity remains constant
Algae extract CO2 until pH 10-11
During dark hours algae produce CO2

## Slide 36
Respiration exceeds photosynthetic process
CO2 production tends to reduce pH
Boiler Waters
CO2 insoluable in boiling water  Removed with steam increase pH

## Slide 37
Alkalinity shift from
Bicarbonate carbonate
Carbonate hydroxide
When there is OH- alk. pH is high pH=11