## Slide 1: ENVE 201 Environmental Engineering Chemistry 1
ACIDITY
Dr. Aslıhan Kerç

## Slide 2: Acidity
Natural waters
Domestic wastewater
Industrial Wastes
Acidity is the ability of water to neutralize bases.
End point for carbonic acid  stoichiometric end point @ pH 8.5
Buffered by
CO2 and HCO3 system

## Slide 3
All water < pH 8.5 contain acidity.
Reference point  phenolphthalein end point
8.2 -8.4
Acidity of natural water is caused by CO2 or by strong mineral acids.

## Slide 4: Carbonic Acid Titration Curve
@ pH 7 considerable CO2 remains to be neutralized.
Carbon dioxide alone will not depress pH below 4
For strong acid  neutralization is completed@ pH 4

## Slide 5
Acidity of natural waters caused by :
  CO2
  Strong mineral acids
  10
  9
  8
  7
  6
  5
  4
  3
  2
  1
CO2 acidity
Phenolphthalein endpoint
Methyl orange end point
Mineral Acidity

## Slide 6
If there is H2CO3 pH doesn’t drop below 4
If pH < 4  Mineral acidity
CO2
Normal component of natural waters.
From atmosphere (Henry’s Law)
Produced from biological oxidation ( End product of both aerobic and anaerobic bacterial oxidation)

## Slide 7
Groundwater high in CO2 since it is not free to escape to atmosphere.
30-50 mg /L can be found.
For groundwater that do not contain Ca, Mg
Ca, Mg neutralize the CO2 through formation of bicarbonates.
CO2 + CaCO3  Ca2+ + 2HCO3

## Slide 8
Mineral Acidity  in industrial wastes
(sulfuric acid , salts of sulfuric acid)
Conversion of sulfur , sulfides, iron pyrites to sulfuric acid and sulfates by sulfur oxidizing bacteria.
2S+3O2+2H2O bacteria 4H++2SO42-
FeS2+3 ½ O2+H2O bacteria Fe2++2H++2SO42-

## Slide 9
Significance of CO2 and Mineral Acidity
Not very important for public health.
CO2 in malt and carbonated beverages higher than natural waters.
If water contain mineral acidity
unpleasant taste
no consumption
Acidic waters  corrosive characteristics
Corrosive factor  CO2
in industrial wastes ; mineral acidity

## Slide 10
CO2 content is also important in lime-soda ash softening,
In biological treatment pH must be maintained (6.0-9.5). Amount of chemicals are calculated based on acidity values.
Combustion of fossil fuels  Nitrogen oxides +Sulfur oxides
When mixed with rain  forms sulfuric and nitric acids.
Acid rain also cause leaching of chemicals (aluminum ) from soil.

## Slide 11
Methods of Measurement
Measured with standard alkaline solutions.
Mineral acids  Titration to pH 3.7 (methyl orange end point) (methyl orange acidity)
Titration till phenolphthalein end point (pH 8.3)  Mineral acidity + acidity due to weak acids.
Total acidity  (phenolphthalein acidity)

## Slide 12
CO2
Special precautions are required for sample collection , handling, and analysis of CO2 .
Partial pressure of CO2 in water is greater that in the atm.
Avoid exposure to air.

## Slide 13
Analyze at the point of collection (min exposure to air min. temp. change)
Collect sample by using submerged tubes, fill completely , leave no air pockets  keep the temp. same.

## Slide 14
Titration Method
To minimize contact with air  titrate in a graduated cylinder.
CO2 will be lost due to stirring.
Take second sample for titration, add required titrant .
Reach final end point slowly.
Pinkish color should persist for 30 s
Excess is siphoned

## Slide 15
Standard reagent NaOH must be free of sodium carbonate.
Neutralization rxn:
2 NaOH + CO2  Na2CO3 + H2O
Na2CO3 + CO2 + H2O  2NaHCO3
If Na2CO3 is originally present  cause wrong results.
For CO2 measurement Na2CO3 sol’n  can be used as standard titrant.

## Slide 16
Calculation from pH and alkalinity
Amount of CO2 can be calculated using ionization eqn. for carbonic acid.
H2CO3 [H+] +[HCO3-]
KA1 = [H+] *[HCO3-] / [H2CO3]

## Slide 17
[H2CO3] = carbonic acid molar content + free carbon dioxide.
CO2 = 99% [H2CO3] ˜= [CO2 ]
Example :
KA1 =4.3*10-7, [H+] =10-7 , [HCO3-] = 4.3*10-3
[CO2 ]= 10-7*4.3*10-3 / (4.3*10-7) = 10-3 mol/L
= 44 mg /L

## Slide 18
Dissolved solidsconcentration must be known.
Require accurate pH measurement
Calculation method
Titration method
for smaller concentration , excessive titration errors
  If CO2 > 2 mg/L  use titration method

## Slide 19
Methyl Orange Acidity
If pH < 4  contain mineral(methyl orange)acidity
Mineral acids are neutralized @ pH 3.7
Bromphenol blue has sharper color change.
E.W CaCO3 = 50
N/50 NaOH is used 1mL = 1 mg acidity
Results are reported as CaCO3

## Slide 20
Phenolphthalein Acidity
Total acidity = mineral acidity + from weak acids
Weak acids are neutralized at pH 8.3
Phenolphthalein or metacresol purple indicators are used
Titrant: N/50 NaOH
Results are expressed as CaCO3.

## Slide 21
Application of Acidity Data
CO2 determination for public water supplies considered for the selection of treatment methods.
Corrosion control
Softening
Industrial wastes  Mineral acidity must be neutralized before discharge
Acidity = N*Vtitrant*50*1000 / ( mL sample)
E.WCaCO3 = 100/ 2 = 50 g/eq