## Slide 1: ENVE 201 Environmental Engineering Chemistry 1
HARDNESS
Dr. Aslıhan Kerç

## Slide 2
Hard waters:
Require considerable amount of soap
Produce scale in hot water pipes , heaters , boilers
Synthetic detergents
 Minimize hard water problem for household
For personal hygiene hard water is problem

## Slide 3
Different equipment are used to prevent scalling problem
Water softenin process
Private and industrial installations
Municipal softening plants (less)
Surface waters are softer than groundwater.
Hardness depends on geological formation.

## Slide 4: Cause and Source of Hardness
Hardness is caused by multivalent cations.
M2+ react w/soap  form precipitates
M2+ + Anions  Scale
Ca2+ , Mg2+ , Sr + , Fe2+ , Mn2+
Al3+ , Fe3+ also contribute to hardness , but their solubility is negligible @pH of natural water.
Hardness of water  due to contact w/ soil and rock

## Slide 5: Methods of Determination
Calculation Method
EDTA Titrimetric Method
Calculation Method
Most accurate method.
Complete analysis of all the cations is required.

## Slide 6
Calculation from concentration of divalent cations.
Atomic Abs. Spect. (AAS)
Inductively Coupled Plasma (ICP)
Ion Chromatography
Ion Specific Electrodes (ISE)
Hardness (mg/L as CaCO3) =
M2+ (mg/L) * 50 / (E.W M2+)

## Slide 7: EDTA Titrimetric Method
Titrating agent : Ethylne diamine tetra acetic acid or its sodium salt.
HOOC-CH2 CH2-COOH
N-C-C-N
HOOC-CH2 CH2-COOH
H H
H H

## Slide 8: EDTA Molecular Structure

## Slide 9
EDTA  chelating agent, forms complexes with Ca2+ , Mg2+ (divalent cations)
Mg2+ + EDTA  [ M.EDTA] complex
Indicator  show excess EDTA , all ions are complexed
Eriochrome Black T (blue color)

## Slide 10
Mg2+ + Eriochrome Black T  ( M. Eriochrome Black T ) complex
Wine Red
As EDTA is added, it makes stable complexes w/ Ca2+ and Mg2+ .
Types of Hardness
Classification in two ways :
According to metallic ion
Calcium and magnesium
2. According to anions associated w/metallic ions.
Carbonate , non carbonate

## Slide 11
Types of Hardness
Classification in two ways :
According to metallic ion
Calcium and magnesium
2. According to anions associated w/metallic ions.
Carbonate , non carbonate

## Slide 12: Calcium – Magnesium Hardness
Ca , Mg cause greatest portion of hardness.
Amount of Mg2+ should be known for lime soda ash softening.
Ca-Mg  Calculated from complete analysis
Total hard.– Calcium hard. = Magnesium hard.

## Slide 13: Carbonate and Non-Carbonate Hardness
Carbonate hardness equivalent to
(bicarbonate + carbonate) alkalinity.
When hardness > CO3 2- +HCO3- alkalinity
Carbonate Hardness = Alkalinity
Excess = Non-carbonate hardness

## Slide 14
Hardness ≤ Carbonate and HCO-3 alk
Carboante hardness = Total Hard
Carbonate Hardness  Temporary hardness
( precipitate at elevated temp., boiling)

## Slide 15
Ca2+ + HCO3-  CaCO3 + CO2+ H2O
Ca2+ +2HCO3- + Ca(OH)2  2CaCO3 + 2H2O
Permanent hardness (Non-carbonate Hardness, NCH) can’t be removed by boiling.
Non-Carbonate Hard.=Total Hard.– Carbonate Hard
Hardness expressed as CaCO3
Non-Carbonate hardness associated w/sulfate, chloride, nitrate anions.

## Slide 16: Pseudo- Hardness
When there is Na+  interfere with normal behavior of soap.
Na+ is not a hardness causing cation.
High concentration of Na+  Pseudo-Hardness

## Slide 17: Application of Hardness Data
Suitability of water for domestic industrial use
Softening process