## Slide 1: Phosphorus and Phosphate
Phosphorus is essential for the growth of algae and other biological organisms.
Algal blooms P enters into surface waters from,
- Domestic + industrial discharges
- Natural runoff

## Slide 2: Phosphorus and Phosphate
Municipal wastewater contain 4-16 mg/L phosphorus as P

## Slide 3: Forms of phosphorus found in aqueous solutions
Orthophosphate
PO4 3-, HPO4 2- , H2PO4-, H3PO4
Polyphosphate
2 or more P atoms + O2 atoms + (H) combined in a complex molecule
Organic Phosphate
Minor

## Slide 4
* Orthophosphates are available for biological metabolism without further breakdown

## Slide 5
Polyphosphate Orthophosphate
Hydrolysis (slow)
* Organic Phosphate : minor in domestic ww
* Found in industrial wastes and ww sludges

## Slide 6
* Orthophosphate determined colorimetrically
* Ammonium molybalate
Colored complex with phosphate
* Polyphosphate, organic phosphate must be converted to orthophosphates using acid digestion

## Slide 7: The Phosphorus Cycle
* Cycles between organic and inorganic forms (like nitrogen cycle)
* Organic compounds containing P are found in all living matter
* Orthophosphate PO4 3- Readily used

## Slide 8: The Phosphorus Cycle
Phosphorus cycle has two major steps
Conversion of organic to inorganic
Conversion of inorganic to organic P

## Slide 9: The Phosphorus Cycle (continue)
* Conversion of insoluble forms of phosphorus such as calcium phosphate Ca(HPO4)2 into soluble forms principally to PO43- is also carried out by microorganisms
* Organic P in dead plant and animal tissue, animal waste products is converted bacterially to PO4 3-
* PO4 3- releases to the environment is then incorporated into plant and animal tissue

## Slide 10: Phosphorus in Wastewater Treatment
-Domestic ww rich in P compounds
*Amount of phosphorus released from humans is a function of protein intake. Metabolic breakdown of proteins and elimination of the liberated phosphates in the urine
1.5 g /day-capita

## Slide 11: Phosphorus in Wastewater Treatment (continue)
- Synthetic detergents contain
Phosphorus 12-13 %
Polyphosphates 50%
* Substitution of soap with synthetic detergents increased phosphorus content of domestic ww 2-3 times much in inorganic phosphorus content

## Slide 12: Phosphorus in Wastewater Treatment (continue)
- Microorganisms in biological process of wwtp require P for reproduction and cell tissue synthesis. Municipal ww have enough P, but industrial wastes may not have enough
- Add inorganic phosphate for this deficiency in the form of H3PO4

## Slide 13: Phosphorus in Wastewater Treatment (continue)
Fertilizers
WWTP digested sludges Rich in N&P
- BNP Process

## Slide 14: Phosphorus in Wastewater Treatment (continue)
Phosphorus Determination is important for,
Corrosion prevention, control of boiler’s scale
Assessing the potential biological productivity of surface waters
Eutrophication control
WWTP effluents
Operation of WWTP
Stream Pollution Control