## Slide 1: SULFUR AND SULFATE
ENVE 202
Dr. A. Kerç

## Slide 3: SULFATE
One of the major anions occuring in natural waters
Cathartic effect müshil etkisi
Upper limits  250 mg/L

## Slide 4: SULFATE (continue)
Important for public + industrial water supplies  due to tendency of water to form scaling in boilers and heat exchangers
Two serious problems in ww.Odor
sewer corrosion

## Slide 5: SULFATE (continue)
Reduction of sulfates to hydrogen sulfide under anaerobic condition
SO4-2 + org.matter S-2 + H2O + CO2
S-2 + H+  HS
HS- + H+  H2S
(Primary ionization cons. KA1 = 9.1x10-8 )
Anaerobic bact

## Slide 6: SULFATE (continue)
In biochemical oxidation ( for anaerobic ) if DO and NO3- do not exist, sulfates serve as oxygen source (electron acceptor)
Relationships between H2S, HS- , S-2 are pH dependent

## Slide 7: SULFATE (continue)
If pH > 8 HS- and S-2 [(H2S) is small]  no odor problem
If pH < 8 equilibrium shift right  @pH 7 80% H2S
If concentration > 20 ppm toxic

## Slide 9: Sewer Corrosion
High temperature, long detention timessulfate cause crown corrosion in concrete sewers
H2S responsible (indirectly) for crown corrosion
H2S is weaker than carbonic acid little effect on good concrete

## Slide 11: Sewer Corrosion (continue)
Gravity sewers provide unusual environment
Biological changes occur during transportationrequire oxygen
If well vent. no problem
H2S + O2  H2SO4

## Slide 12: Methods of Analysis
Ion chromatograph
Formation of insoluable BaSO4
According to the quantity of BaSO4 formation
  Gravimetric  precipitate is weighed
  Turbidimetric
Methylthymol blue method

## Slide 13: Methods of Analysis (continue)
Gravimetric : > 10 mg/L
Ba+2 + SO4-2  BaSO4
Add BaCl2 in slight access
Acidify w/HCL  eliminate BaCO3 ppt
Keep near boiling point

## Slide 14: Methods of Analysis (continue)
Excess BaCl2  common ion effect
Formed BaSO4  colloidal form can not be removed by filter
Digestion @ temperature near boiling point  crystalline forms
Filter the crystals with special filter

## Slide 15: Methods of Analysis (continue)
Turbidimetric :
Colloidal formation is enhanced in the presence acidic buffer solution
(Magnesium chloride, potassium nitrate, sodium acetate, acetic acid)
Calibration curve

## Slide 16: Methods of Analysis (continue)
Automated Methylthymol Blue
Continuous flow analytical instrument
BaCl2 added @low pH BaSO4
pH adjusted to 10
Methylthymol blue added

## Slide 17: Methods of Analysis (continue)
Combines with excess Barium  blue chelate
Umcomplexed methylthymol blue remaining  grey color (automatically measured)